## Slide 1
AUSIGN: An Auslan Interpreter Glove
Empowering communication through wearable technology
BY RAHUL RAMACHANDRAN AND ENZO MORIGUCHI

## Slide 2
WHY DOES AUSIGN EXIST?
User Needs
  Real-time Auslan-to-speech
  Portable, offline, affordable
  Emotion/context inference
  Intuitive, day-long use
Limitations of Current Solutions
  Expensive (e.g. Brightsign glove ≈ $6,800 AUD)
  Mostly support ASL, not Auslan
  Require phones/internet, lack context awareness

## Slide 3
WHO IS AUSIGN FOR?
Target: Auslan users aged 25–59 needing daily, affordable communication tools
User Validation
(21 Respondents)
  67% currently use aids
  Avg usefulness: 6.1/10
  Openness to new devices: 8.2/10
  62% interested in AUSIGN
Market Opportunity
  16,000 Auslan users (2021 Census)
  3.6M Australians with hearing loss → 7.8M by 2060
  Interpreter costs ≈ $127.50/hr
  Existing solutions out of stock, ASL-only

## Slide 4
Key Requirements
  ≤ 50g per glove
  ≥ 12 hours battery life
  ≥ 90% translation accuracy
  ≤ 2 seconds latency
  Offline functionality
  Under $100 manufacturing cost
  Customizable settings (volume, dialect)
  Emergency signal support

## Slide 5
Product and Design Concepts
  Flex sensors + IMU = accurate gesture detection
  Heartbeat sensor = emotional context
  ESP32 = processing + Bluetooth for personalization
  Onboard speaker + optional LCD feedback
  Custom mapping of signs
  Emergency button (e.g., “Help”)
Design Highlights

## Slide 6
Unique Selling Points
  Auslan-specific – Not ASL-focused like competitors
  Context-aware – Heart rate input for emotion detection
  Gesture + Motion Fusion – Flex + IMU improves accuracy
  Lightweight & Comfortable – Under 50g
  Bluetooth-Enabled – Mobile app for personalization
  Offline Support – Usable without internet
  Custom Sign Training – Adaptable to regions/users
  Affordable – Sub-$100 vs $6,800 competition

## Slide 7
High-Level Block Diagram

## Slide 8
Subsystem | Component | Notes
MCU | ESP32-WROOM-32 | I2C, UART, ADC, Bluetooth
Finger Sensor | 3” Flex Sensors | 25k–100kΩ resistance range
Motion Sensor | MPU6050 IMU | 6-axis detection
Biometric Sensor | MAX30102 | Heart rate & oximeter
Output | 3W Speaker, 20×4 LCD | Compact + intuitive UI
Power | TP4056 + LiPo + MT3608 | USB charging + 5V boost
Input | Tactile Push Button | Emergency signal
Technical Components

## Slide 9
Financial Plan
  ESP32: $8
  Flex Sensors ×5: $20
  MPU6050: $5
  MAX30102: $6
  Speaker + Amp: $4
  LCD: $7
  Power Circuit (TP4056 + MT3608): $3
  Misc (PCB, Glove Material, Button): $15
  → Total: ~$68 AUD
Per Unit Manufacturing Estimate
Selling Price: $150–200 AUD
NPV: Viable pricing based on competitor comparison
Profit Margin: ≥ 100%, with accessibility focus

## Slide 10
Development Plan
Week 6–7
  Hardware Integration (Flex + IMU + HR + Speaker)
  Sensor Calibration
Week 8
  Real-time Auslan-to-Speech Mapping
  Bluetooth App UI + Emergency Button Logic
Week 9
  Context Awareness Logic (Heart rate threshold)
  Output testing with user trials
Week 10
  Final Testing + Demo
  User Feedback + Iteration
  Presentation and Documentation
Team Allocation:
  Hardware: Enzo
  Firmware + Possible ML Model: Rahul
  App + UI: Rahul
  PCB: Enzo
  Integration & Testing: Both